## Slide 1
CHIPCRAFT 3.0 — RTL TO PHYSICAL DESIGN HACKATHON
SMART WATER
DISTRIBUTION SCHEDULER
Priority-Aware · Emergency-Ready · Conflict-Free Valve Control
TEAM LOGIC DUO | Team #32
Akif Mohamed (Team Lead) · [ add teammate name ]
Government College of Engineering, Srirangam
Flow: Verilog RTL → VCS Simulation → DC Synthesis → ICC2 Layout (SAED 32nm)
Notes: Good morning! We are TEAM LOGIC DUO from Government College of Engineering, Srirangam. Our problem is the Smart Water Distribution Scheduler. [Say your teammate's name too — and remember to type it on this slide first!]

## Slide 2
SLIDE 2
ROUND 0
PROBLEM STATEMENT
Design a controller that schedules water to multiple zones
based on DEMAND, PRIORITY and AVAILABLE SUPPLY.
It serves the most urgent zone first, opens only ONE valve at a time,
and never wastes water when supply is short.
Why it matters:
In real cities, low-pressure zones wait while high-pressure zones overflow.
Our chip makes distribution FAIR, SAFE and ACCOUNTABLE.
Notes: The PS in two lines: Design a controller that schedules water to multiple zones based on demand, priority and available supply — serving the most urgent zone first, opening only one valve at a time, and never wasting water when supply is short. That's it. Simple, but every objective in the PS has to be covered.

## Slide 3
SLIDE 3
ROUND 0
OUR INNOVATIVE SOLUTION
🏆 Priority + Emergency Arbiter
4 zones, priority 0-3. Priority 3 = EMERGENCY jumps the queue. Tie-break: lowest zone index — fair and deterministic.
🔒 Conflict-Free One-Hot Valves
Exactly one valve can open at a time (one-hot by design). A running flush is never aborted — valve safety first.
🧠 SMART Skip-to-Fit Scheduling (our innovation)
If the top zone's demand > available water, we serve a smaller zone that FITS instead of stalling the whole city. No starvation!
📊 Accountability Built-In
Total + per-zone cycle counters and a LIVE insufficient-supply flag. Every litre served is tracked — audit-ready.
Design: FSM (IDLE → SERVE → WAIT/DONE) + demand tracker + priority arbiter + one-hot valve driver + counters
Plan: clean synthesizable Verilog for 32nm, covered by a self-checking testbench (7 test groups) across the full RTL→GDS flow
Notes: Our solution has four building blocks. Two are required by the PS — the priority arbiter with emergency support, and the one-hot valve safety. Two are OUR innovation: first, skip-to-fit scheduling — if the biggest emergency zone needs 200 units but only 100 are available, we don't stall the city; we serve a smaller zone that fits and flag the shortage. Second, accountability — total and per-zone counters plus a live insufficient-supply flag. It's a simple FSM — tiny and fast for 32nm, and the whole plan maps cleanly onto the RTL-to-GDS flow.

## Slide 4
SLIDE 4
ROUND 0
INTERFACE — INPUTS, OUTPUTS & PARAMETERS
SIGNAL | WHAT IT IS
clk, rst_n | 100 MHz clock, async reset
zone_req[3:0] | zone demands water (one bit/zone)
zone_prio[7:0] | 2-bit priority / zone (3 = EMERGENCY)
zone_demand[31:0] | 8-bit water units wanted per zone
supply_avail[7:0] | water units available now
supply_valid | pump ON
INPUTS
SIGNAL | WHAT IT IS
valve_open[3:0] | one-hot valve commands (safe!)
grant_ack[3:0] | pulse: that zone is served
cycles_done[31:0] | total completed cycles
zone_cycles[63:0] | 16-bit cycle count per zone
insufficient | 1 = demand but not enough water
busy, status[2:0] | serve in progress; state code
OUTPUTS
SIGNAL | WHAT IT IS
NZONES = 4 | number of zones
DATA_W = 8 | water unit width (0–255)
SERVE_CYCLES = 16 | clocks per distribution
Clock = 100 MHz | 10 ns, SAED 32nm
KEY PARAMETERS & VALUES
STATUS CODES
0 = IDLE (nothing to do)
1 = SERVE (valve open, water flowing)
2 = WAIT (insufficient supply)
3 = CYCLE DONE (bookkeeping pulse)
PRIORITY VALUES
0 = Low · 1 = Medium · 2 = High · 3 = Emergency
Notes: Our interface. Inputs: each zone sends a request, a 2-bit priority and its demand in water units. The plant sends available supply and pump status. Outputs: one-hot valve commands — the safety core of our design — an ack pulse when a zone is served, total and per-zone cycle counters, and a live insufficient-supply flag. Everything is parameterized: 4 zones, 8-bit demands, 16-clock serve time, 100 MHz target.

## Slide 5
SLIDE 5
ROUND 0
EXPECTED OUTCOMES & KEY VALUES
→ PS objectives to be covered
target 6 / 6
→ Self-checking TB (7 test groups)
expected ALL PASS
→ Valve conflicts (one-hot)
expected 0 conflicts
→ Priority + emergency behaviour
served first, by design
→ Insufficient-supply handling
flag + WAIT + skip-to-fit
→ Cycle tracking accuracy
total = Σ per-zone
→ Clock target (SAED 32nm)
100 MHz / 10 ns
→ Logic style
Synthesizable Verilog, no latches
→ Synthesis (DC)
expect: timing met + clean QoR
→ Physical design (ICC2)
expect: P&R clean + GDS
→ Final deliverables
RTL+TB+SDC+Netlist+Rpts+GDS
→ Design area class
4-zone controller, 32-bit counters
EXPECTED BOTTOM LINE:
A fair, safe and auditable water scheduler — all 6 objectives met, RTL verified, timing-closed 32nm layout at 100 MHz.
Notes: What we EXPECT to deliver. All six PS objectives covered. A self-checking testbench with 7 test groups, targeting all pass. By design the valves are one-hot, so we expect zero conflicts. The counters will be exact: total equals the sum of per-zone counts. Technical targets: 100 MHz in SAED 32nm, latch-free synthesizable Verilog, timing-closed synthesis in DC and clean place-and-route with GDS in ICC2. Expected bottom line: fair, safe, auditable.